## Slide 1: Pose Graph Optimization for Vision-Only Freehand 3D Ultrasound Reconstruction
Update 01.06.2026
Jannis Meyer

## Slide 2: Reminder
Pose predictions
  Ti
  Ti→i+1
US Frames
FVs
US frames
PGO
T0
T2
T3
T1
T2→3
T1→2
T0→1
T0→2
T1→3
TUSREC24/25
DualTrack (winner of TUSREC25)
2
Notes: Reminder
US frames from TUSREC data for now
DT model for now
Get pose predictions and more from that
Build pose graph and optimize using extra constraints and weights

## Slide 3: What did I do?
Set up DualTrack code (+PGO) using GTSAM library
Set up TUSREC24/25 data
Evaluations on DualTrack and TUSREC2/25 data
Writing Master Thesis
3

## Slide 4: Pose Graph Optimization
Optimization formula:
(no weights for simplicity)
➔ , set of variables to optimize
➔ , Jacobi matrix ,
➔ Linear optimization problem
➔ , compute for minimum , update , redo until converges
4
Notes: More mathematical insights into PGO
Base optimization formula from last time
More general formulation
Linear optimization problem
Internal functionality of GTSAM

## Slide 5: Pose Graph Optimization
Optimizer:
Levenberg-Marquardt: Additional factor to Jacobi-matrices for more control of optimization
λ
Weights:
Prior (first node): 6*105
Rest: 6*102
➔ Base line PGO, no individual weighting nor additional edges yet
5
Notes: Parameters for PGO right now
No extra edges or weights

## Slide 6: Error metrics in DualTrack
Final Drift Rate (FDR):
Error between pose prediction and GT of final frame (translation only)
Common error metric in 3D US reconstruction
Global Point Error (GPE):
“Average point error between the true position and the fully reconstructed trajectory estimate at each timestep”
Mentioned in DualTrack paper and TUSREC challenge
(Error equals Euclidian distance between estimated and GT point, regarding center and four corners)
6

## Slide 7: Evaluations
 | DualTrack24 | DualTrack25 | DualTrack24 with PGO | DualTrack25 with PGO
TUSREC24 Validation Data (72 scans) | FDR: 5.1% GPE: 4.92mm (also stated in paper) | FDR: 28.5% GPE: 24.51mm | / | FDR: 28.6% GPE: 24.64mm
TUSREC25 Validation Data (six scans) | FDR: 488.8% GPE: 56.53mm | FDR: 72.9% GPE: 9.45mm (9.2mm stated in paper) | / | FDR: 72.5% GPE: 9.43mm
*FDR and GPE averaged over all scans
7
Notes: See results
PGO on DT24 currently not possible as DT24 code doesn’t provide individual results for a single frame, just overall
No GPE for PGO results as I didn’t have the time yet to implement that

## Slide 8: Explanations of Results
Bad FDR for 25/25:
Euclidean distance
Complex scanning motion
TUSREC challenge rating does not evaluate FDR
Low performance for cross-evaluation:
Different TUSREC24 and TUSREC25 data sets
No calibration or retraining of models
Near-zero dis-/improvement from PGO:
Base line, perfect consistency of graph
8

## Slide 9: Next steps
Writing Master thesis
Fit DualTrack code to my needs
Improve PGO/Implement actual PGO
(Evaluate on TUSREC training data)
9

## Slide 10: Sources
https://github-pages.ucl.ac.uk/tus-rec-challenge/
https://arxiv.org/pdf/2509.09530/
https://borglab.github.io/gtsam/
https://borglab.github.io/gtsam/nonlinearoptimizer/
https://borglab.github.io/gtsam/betweenfactor/
10