## Slide 1: Pose Graph Optimization for Vision-Only Freehand 3D Ultrasound Reconstruction
Update 01.06.2026
Jannis Meyer

## Slide 2: What did I do?
Enhance Image Registration (IR) (SimpleITK, rigid transform, only 2D so far!)
  Metrics, optimizers, techniques, parameters
Evaluate IR on whole scans (no application to PGO here yet): Find frame poses only using IR
Writing Master Thesis
2

## Slide 3: Image Registration: Basics
3
Find transform which makes one image align with another
Source: https://www.researchgate.net/figure/Basic-example-of-an-image-registration-procedure-F-is-the-target-image-M-is-the-image_fig4_320212021
F: fixed, M: moving
➔ SimpleITK: Finds TM➔F

## Slide 4: Image Registration: Combination of transforms
4
IR works in 2D and gives 3DoF transforms (x, y, yaw)
Volume reconstruction works in 3D and needs 6DoF transforms (x, y, z, pitch, yaw, roll)
➔ Combine 2D IR pose and 3D DualTrack pose:
IR
DualTrack
4
!
r0 | r1 | r2 | tx
r3 | r4 | r5 | ty
r6 | r7 | r8 | tz
0 | 0 | 0 | 1
r0 | r1 | tx
r2 | r3 | ty
0 | 0 | 1
r0 | r1 | r2 | tx
r3 | r4 | r5 | ty
r6 | r7 | r8 | tz
0 | 0 | 0 | 1
x, y, yaw
z, pitch, roll

## Slide 5: Image Registration: SimpleITK
What works best so far (SimpleITK):
Metric: Mattes Mutual Information
  Maximize information between fixed and moving image
  Compute fixed, moving and joint PDFs over set of intensity bins, compute MI by summing over bins
  50 histogram bins
Optimizer: Gradient Descent
  Init with pose estimation from DualTrack (init with identity works almost equally well)
  Learning rate 0.1, min. change 1e-4, 200 max. iterations
5

## Slide 6: Image Registration: Results
Norm of translational vector Angle of the rotation
6
Notes: TUSREC24, 72 scans
Slight correlation between transform magnitude and error, especially for large values

## Slide 7: Image Registration: Results
Blue: GT
Yellow: IR
7
Notes: TUSREC24, one scan, first 100 frames
general trend is fine
Note: z, pitch, roll from DualTrack: No jitter

## Slide 8: Image Registration: Results
8
Notes: TUSREC24, one scan each
General direction is fine
Again no jitter for DualTrack
IR retains jitter

## Slide 9: Image Registration: Problem
Problem:
2D IR does not account for out-of-plane motion (z axis) nor pitch and roll
y y
x
x z
➔ Features present in one picture are not necessarily present in the other (spawning feature problem)
➔ 2D IR cannot find a transform which makes the two images align perfectly
➔ GT transform will not yield a perfect error metric
9

## Slide 10: Counter measures
10
Focus on center
Use only center for IR
➔ Center 50% of both x and y
➔ Pixels near to the center are less affected by roll and pitch (center of rotation is the image center)

## Slide 11: Counter measures
11
Focus on center

## Slide 12: Counter measures
12
Patch and evaluate
Divide fixed and moving into patches
For every fixed patch:
  Apply ref transform from DualTrack
  Compare transformed fixed patch and corresponding moving patch
  Consider for IR if similar
➔ 4x4 grid, Normalized Cross Correlation for comparison (value range [-1, 1]), threshold 0.7
➔ Patches with little similarity (due to a potential spawning feature) are discarded

## Slide 13: Counter measures
13
Patch and evaluate
White: keep
Black: discard
Notes: - black: discard

## Slide 14: Counter measures
14
Focus on center
Improvement of >200% for FDR, GPE and run time for TUSREC24, 72 scans
Patch and evaluate
Improvement of 5% for FDR, 1,5% for runtime for TUSREC24, 72 scans
➔ But: IR still performs worse than DualTrack
➔ TUSREC24, 72 scans:
DualTrack24: FDR 5.1mm, GPE 4.9mm
IR with counter measures: FDR 11.4mm, GPE 9.9mm

## Slide 15: Error evaluations
15
Abs GT vs Abs Error
(DualTrack24 in-between Pred – GT, TUSREC24 72 scans combined)
➔ Again: Larger error for larger values

## Slide 16: Error evaluations
16
Mean Error Through Time
(DualTrack24 in-between Pred – GT, TUSREC24 72 scans combined)
➔ Mean error of DualTrack is ~0 for all 6DoF
Notes: translation: mm; rotation: angle

## Slide 17: Error evaluations
17
mm, º | X | Y | Z | Pitch | Yaw | Roll
GT | 0.244 | 0.0343 | 0.198 | 0.034 | 0.031 | 0.036
Error | 0.058 | 0.021 | 0.069 | 0.032 | 0.025 | 0.029
Ratio (Error/GT) | 23.8% | 61.2% | 34.8% | 94.1% | 80.6% | 80.6%
GT vs Error mean absolute value for every 6DoF
(DualTrack24 in-between Pred – GT, TUSREC24 72 scans combined)
➔ Relative largest errors happen for y and pitch
➔ Larger relative errors for rotation than translation

## Slide 18: Error evaluations: Speculations
18
➔ Images are 640x480 pixels (x, y)
➔ Less information on y axis, larger error for y and pitch
➔ Translation is easier to estimate as x and y are directly deductible from images

## Slide 19: Next steps
19
Improve 2D IR
Combine with PGO
  Jitter?
  Error?
Try 3D IR
Write Master Thesis